## Slide 1: GEM 4000 Stress Test Configuration
Product | SBC | H.W. | Ver. | Stable | Unstable | Total #
G4K | New Seco | Product | V3.1 b24 | 1 | 10 | 11
G4K | Old Seco | Product | V3.1 b24 | 1 | 17 | 18
G4K | Kontron | Product | V3.1 b24 | 1 | 2 | 3
Server | G8 | Virtual | V5.1.0 b30 | 1 | N/A | 1
Note: Sample frequency is16 samples an hour.
Deviation: Four instruments crashed before network up/down script was applied.

## Slide 2: GEM 4000 Failure Rate Trend
GWP5.1.0 b36, G4K b24 | Stable | Unstable | Overall
Baseline | 0.0% | 0.4% | 0.3%
2 Day Run
Chart: 
| GWP 5.1.0 b26, G4K b22 | GWP 5.1.0 b26, G4K b24 | GWP 5.1.0 b26, G4K b24 | GWP 5.1.0 b30, G4K b24 | GWP 5.1.0 b36, G4K b24 | GWP 5.1.0 b40, G4K bDev | GWP 5.1.0 b40, G4K b24 | GWP 5.1.0 b40, G4K b24
Stable | 0 | 0 | 0.014 | 0 | 0 | 0 | 0.071 | 0.067
Unstable | 0.043 | 0.01 | 0.026 | 0.016 | 0.004 | 0.027 | 0 | 0.021
Overall | 0.023 | 0.005 | 0.02 | 0.008 | 0.003 | 0.025 | 0.04 | 0.025
4 Day Run Scripts Partially running

## Slide 3: GEM 4000 Failures and Frequency
CR# | Type | Summary | Frequency
18622 | Crash | Multiple 3206 on analyzer before restart. 1:00 AM. | 6
17797 | Freeze | Java Freeze | 1
GWP 510
Error Type | New | Old | Kontron
Crash | 2 | 0 | 2
Freeze | 0 | 0 | 0
Stable Network
Error Type | New | Old | Kontron
Crash | 2 | 0 | 0
Freeze | 0 | 1 | 0
Unstable Network